SECTION 720	-	LANDSCAPE WORKS

##This section cross-references Sections 176, 204 and 750.

If any of the above sections are relevant, they should be included in the specification.

If any of the above sections are not included in the specification, all references to those sections should be struck out, ensuring that the remaining text is still coherent:

720.00	GENERAL

This section covers the requirements for works associated with the vegetation of the site.  This includes, but is not limited to, material supply, site preparation, mulching, planting, grassing, irrigation and landscape maintenance as specified and shown on relevant Drawings, Planting Details and Schedules.

720.01	DEFINITIONS

(a)	Caliper

The stem or trunk diameter of a tree at a nominated point.  Caliper is measured at 300 mm above ground for sizing of nursery plants.

(b)	Independent Expert

An expert independent of the contractor suitably qualified in environmental, agricultural or soil science, land rehabilitation or landscape architecture.

(c)	Indigenous Plant

A species listed on the planting schedule that is likely to have existed pre-1750 no more than 10 km from the site.

(d)	Individual Tree Planting

Any tree planting of single trees each surrounded by a mulch ring and/or grass cover.

(e)	Planting Area

Any continuous area where multiple plants are established using stock from containers such as pots, tubes and cells or by direct sowing (other than grassed areas).

(f)	Propagule

A propagule is any plant part capable of producing a new plant (e.g. seeds, cuttings, bulbs, corms, rhizomes, etc).

(g)	Topsoil

The weathered surface layer of soils that includes organic matter.

(h)	Tube stock or cell stock

Plants grown in small (less than 0.5 litre) containers.

(i)	Weed

Any plant which is not desired as follows

(i)	Declared weed.  Any plant that is a declared weed under as defined in the Weed Management Act 1999 in respect of the project area.

(ii)	Species or individual plants specified to be removed.

(iii)	Weeds of planting beds and around individual trees include any plant not specified in the planting schedule or is not indigenous to the site.  This includes all local environmental weeds and declared weeds.

(iv)	Regionally declared environmental weeds of grassed areas include all species listed in (i) above, broadleaf species (except broadleaf species specified for sowing) and other weeds where specifically listed.

720.02	SURVEILLANCE, RECORDS AND REPORTING

The Contractor must engage an independent expert to undertake surveillance and auditing of the landscaping and plant maintenance works. The Contractor will prepare a schedule for the independent expert to inspect and audit that will ensure compliance with this specification in accordance with the landscaping and plant maintenance timeframes.

The Superintendent must be notified at least 2 working days prior all inspections and review of samples required in accordance with the independent expert schedule.  Samples, records and certificates shall be provided to the Superintendent at least 10 working days prior to bulk delivery.

***	The Contractor shall provide the following before commencement of the relevant landscape work: ##[strikethrough inapplicable items below]:

(a)	Inspections

(	plant stock for all plant species

(b)	Samples

(	mulch

(	imported topsoil.

(c)	Records

(	evidence of origin of indigenous provenance plant material

(	analysis certificates for grass seed

(	details of suppliers

(	soil tests on topsoil

(	copies of fertiliser labels.

720.03	SUPPLY OF MATERIALS

(a)	Site Topsoil

Site topsoil shall be used wherever possible, in preference to imported topsoil.

(b)	Soil Testing

Soil testing is to be undertaken to establish what soil amendments and macro and micro-nutrients are required to be added to the topsoil to support normal healthy plant growth.

The Contractor shall have sampling, assessment and interpretation of soil test results carried out by a Certified Professional Soil Scientist (CPSS), or soil scientist or agronomist with qualifications relating to soil science, and at least ten years relevant experience in soil assessment and management.

(c)	Supply of Imported Topsoil

Where soil testing determines that site topsoil cannot be ameliorated to achieve the required growth performance targets or is of insufficient quantity to achieve the specified topsoil depth, imported topsoil can be used only to the extent necessary to address the deficiency.

Imported topsoil shall comply with the properties described in Table 720.031:

Table 720.031 Imported Topsoil Blend Supply Properties

| Property | Requirement |
| --- | --- |
| General Requirements | Must be suitable for supporting healthy plant growth of the specified and scheduled species. |
| Texture | The texture shall either match the site topsoil texture or provide a light to medium friable sandy loam with a clay content of 10-15%, capable of handling when moist but lacking cohesion so that it will fall apart easily. |
| Extraneous Material and Contaminants | The topsoil shall be free of sods of subsoil, rubbish, petrol and oil contaminants, lime etc, and meet the requirements for clean fill in EPA Victoria publication 448-Classification of Wastes as ‘Fill Material’ and shall have contaminant levels less than the concentration listed in Table 2 of that document. Stones shall be <5% (by dry weight) with stone size not exceeding 25 mm. |
| Dry Bulk Density (kg/m3) | Bulk density shall be >1000. |
| Soil Nutrients | Adequate levels to support normal plant growth for the scheduled species. |
| Organic Matter (% by mass) | Decomposed matter shall be 3-15% by mass, and undecomposed matter shall be <5% by mass. |
| Weed Content and Pathogens | Soil shall meet AS 4419 5.4. No declared weeds, declared seed or Phytophthora cinnamomi. |
| Wettability (mm/min) | Soil shall meet AS 4419 5.5 |
| Soil pH | 5 – 8 |
| Phosphorous (mg/kg Olsen method) | 5-10 |
| Electrical Conductivity (dS/m) | Soil shall meet AS 4419 5.6 |
| Dispersibility Category | Soil shall meet AS 4419 5.11 |
| Nitrogen Drawdown (NDI150) | Soil shall meet AS 4419 5.12 |
| Permeability | Soil shall meet AS 4419 5.13 |
| Toxicity | Soil shall meet AS 3743 |

(d)	General Supply of Plant Stock

All plants shall be of the type, height, container size and trunk caliper specified in the Plant Schedules, Specification and Planting Plans and shall comply with the properties described in Table 720.032:

Table 720.032  Plant Stock Supply Properties

| Property | Requirement |
| --- | --- |
| General Requirements | All plants shall be hardened off for a minimum 4 weeks in conditions matching prevailing conditions on the Works site. |
| Species Integrity and Labelling | Plants shall be true to type and clearly labelled with at least one label per species per delivery batch. |
| Container Supply Sizes | Tubes shall be at least 0.2 litres in volume. Cells shall be at least 0.08 litres in volume. Other sizes shall be as specified. |

(Table continued next page)

Table 720.032  Plant Stock Supply Properties  … continued

| Property | Requirement |
| --- | --- |
| Root Ball Occupancy | Roots shall be adequate to fill the container. Samples shall demonstrate that >85% of soil volume remains intact when the unsupported rootball is shaken. |
| Root Ball Integrity | Plants shall display a large, well developed and healthy fibrous root system with repeated and sequential division with no evidence of root curl, restriction or damage. The root ball shall not be pot bound and shall generally have roots penetrating to the edge of the pot. Except for monocots with fibrous root systems, plants with girdling, spiralling or j-rooting present in root systems will not be acceptable. |
| Uniformity of Plant Growth | The size shall be in proportion to the container size and species. Tube stock and cell stock shall not have shoot height greater than 3 times the depth of the container. |
| Caliper | Trees shall be self-supporting. |
| Health and Vigour | Plants shall show vigorous tip growth and foliage size, texture and colour consistent with that shown in healthy specimens of the species. Plants shall have undamaged limbs and trunk. |
| Free of Pests and Diseases | Plants shall be free from pests and diseases at time of delivery, with visible attack from previously eliminated pests and disease restricted to <10% of foliage such that long term success of the plant is not affected. |
| Weed Free | Plants shall be provided in containers free of weeds. |

(e)	Indigenous Plant Stock

The Contractor shall source seed or other propagules for indigenous plant stock from within or as close to the site as practicable and from areas with similar soil type (same parent material) and rainfall (to minus 100 mm ARI).  Seed shall be collected in accordance with Florabank Guidelines and Codes of Practice (http://www.florabank.org.au/) and shall not be collected more than 25 km from the site.  Grasses and wetland species may be sourced up to 50 km from the site in areas with the same soil type and similar or lower annual rainfall.  Where a distinct form of a species occurs naturally in the local area, that form shall be used.

The Contractor shall submit documentation of origin of indigenous provenance plant material which shall include the following details for each seed lot:

(	species name

(	storage code

(	collection locality - Latitude/longitude

(	approximate number of parent plants sampled

(	approximate number of plants in that local population.

All seed lots of the same species collected at different localities shall be supplied as separate seed lots.  The provenance shall be tracked through propagation to planting for possible future seed collection purposes.

The format of the seed collection records shall be a spreadsheet compatible with Microsoft Excel.

(f)	Pesticides

Herbicides applied as a spray shall include sufficient coloured dye to identify application areas for at least 5 days.

(g)	Compost

Compost may be substituted in the event where either site topsoil or imported topsoil is deemed by independent expert advice to be unlikely to provide an adequate growth medium to meet the plant growth targets of 720. 10 and 720.11 or is deemed likely to slump on surfaces greater than 1V:3H.

Compost shall be tested in accordance with AS4454 - 2012.

Compost shall be applied at a minimum depth of 50 mm.

(h)	Fertilisers

Fertilisers for newly grassed areas shall be N:P:K 10:4:6 with trace elements.

Fertilisers for planting areas and advanced trees shall be slow release with a 9-12 month release period and suitable for the establishment of plant types, sizes and species specified in the plant schedules.

(i)	Gypsum

Only manufactured gypsum (Calcium Sulphate) shall be used with gypsum derived from recycled plaster board not be used.  Sodium shall not exceed 1% by mass.

(j)	Wood Mulch (Chipped or Shredded)

All wood mulch shall be supplied, delivered, handled and applied in accordance with AS 4454.

(i)	Imported Wood Mulch

Wood mulch shall comply with the properties described in Table 720.033:

Table 720.033  Shredded or Chipped Wood Mulch General Supply Properties

| Property | Requirement |
| --- | --- |
| General Requirements | Mulch shall meet AS 4454, Table 3.1 for composted or pasteurised mulch. Mulch type shall have fibrous properties which 'interlock' the particles so that installed mulch is not blown away by wind. |
| Purity | Mulch shall be free of soil and weeds, plant pathogens, vermin, treated pine, exposed sharp metal, plastic and other litter, and toxins. Plywood, composite timber product and painted timber shall not exceed a combined maximum of 1% by weight total. |
| Sizing | Meet AS 4454–2012, Table 3.1(A) In planting areas adjacent to either roads posted at <80 km/h, pedestrian or cycle paths or recreational open space, particles shall be no longer than 200 mm with 95% of particle size to be no wider than 40 mm and no longer than 140 mm. In planting areas adjacent to roads posted at ≥80 km/h, particles shall be no longer than 400 mm with 80% of particle size to be no wider than 50 mm and no longer than 140 mm. |

(ii)	Site Mulch

Site mulch available from the chipping of on-site indigenous or non-weed vegetation shall be used where possible.  Any species that could have weed potential by seed or vegetative fragments shall not be recycled in the landscape works.  Mulch shall satisfy the purity and sizing requirements shown in Table 720.033.

(k)	Tree Guards, Stakes and Marker Stakes

Tree guards shall be either opaque plastic and of sufficient gauge and UV inhibitor to ensure a minimum two year life or minimum 2 litre cartons of sufficient construction to ensure a minimum 18 month life.  Tree guard stakes and marker stakes shall be sufficiently robust to be driven into the ground, securely support the tree guards and ensure a minimum two year life.

(l)	Weed Control Mat and Erosion Control Mat

The Contractor shall supply and install jute or approved equivalent, biodegradable, fire retardant weed and erosion control mat as indicated on the Drawings or as specified.  Weed Control Mat shall be minimum 700 grams per square metre and Erosion Control Mat shall be 300 grams per square metre.  The surface of the mat shall permit water infiltration.

(m)	Grass Seed

Grass seed shall comply with Appendix A - GRASS SEED PROPERTIES, unless otherwise specified in the Landscape Plan and/or the Erosion and Sediment Control Plan.

(n)	Cover-crop seed

Rye-corn (Secale cereale) seed shall be used as a cover-crop to stabilise areas to be subsequently sown or planted and for the stabilisation of temporary batters and stockpiles.

The quality and specified properties of all seed shall be analysed and certified by either a NATA (National Association of Testing Authorities) or ISTA (International Seed Testing Authority) laboratory.  Labelling of all seed shall comply with the Australian Seed Federation National Code of Practice for Seed Labelling and Marketing.

720.04	PEST AND WEED CONTROL

(a)	Pest and Weed Management Procedures

The Contractor shall develop and implement site specific pest and weed management procedures to control pest and weed populations.  The procedures shall consider pest animals, plants, fungi and other pathogens that may impede plant establishment.

Weed management procedures shall include removal of weeds from their existing locations before, during and after site clearing, topsoil stripping and landscape works.  Weed management procedures shall minimise the spread of weeds in topsoil to other locations within and outside the site.

In addition to Sections 204 and ##176: pest and weed management procedures shall include control of soil borne pathogens including, but not limited to Phytophthora cinnamomi, Armillaria sp. and soil borne weeds.

(b)	General Requirements

Pesticides shall be used in accordance with the manufacturer’s instructions.  Where off-label use of pesticides is considered desirable to achieve pest control requirements, the Contractor shall be responsible for the investigation and procurement of off-label permits.  The Contractor shall advise the Superintendent of any proposed off-label pesticide use prior to pesticide application.

Weed and pest control personnel shall be qualified and experienced in the use of pesticides, control of weeds, prevention of pesticide drift and identification of target and non target species found on site and included in the planting schedules.

The Contractor shall prevent runoff into waterways of pesticides not registered for use in waterways.

If ‘non-target’ areas or plants are damaged during weed control works, then the Contractor shall be responsible for the reinstatement of those areas to the satisfaction of the Superintendent.

(c)	Pre-Planting Weed Control

Pre-planting weed control shall be undertaken to ensure that planting areas and new grassed areas are free of visible weeds prior to the commencement of planting and grassing.  Weed control shall be programmed and implemented to deplete the potential weed seed bank within the topsoil to be used in planting beds.

720.05	SITE PREPARATION

Further to the requirements of Section 204, the Contractor shall provide the soil preparation described in Table 720.051.  All elements of soil preparation proceed in order from left to right.

Table 720.051  Soil Preparation Requirements

| Situation | Initial Ripping of Subsoil Prior to Topsoil Placement | Minimum Topsoil Depth | Cross Ripping | Cultivation |
| --- | --- | --- | --- | --- |
| Planting Areas in disturbed areas flatter than 3h:1v | Min 400 mm deep at max 500 mm spacing. Leave all batters with roughened subsoil to assist with keying of topsoil. | 150 mm | - | Min 150 mm deep |
| Planting Areas in disturbed areas steeper than 3h:1v | Min 300 mm deep at max 500 mm spacing, between parallel to and 45° from contour. Leave all batters with roughened subsoil to assist with keying of topsoil. | 100 mm | - | - |
| Planting Areas in undisturbed areas | Min 400 mm deep at max 500 mm spacing | - | - | Min 150 mm deep |
| Grassing in disturbed areas | Min 200 mm deep, 500 mm max spacing | 75 mm, except 100 mm in swales | Min 100 mm deep, 500 mm max spacing | - |
| Grassing in undisturbed areas | - | - | - | Min 100 mm deep |
| Individual Tree Planting (including advanced trees) within grassed areas. The area of treatment is 25 m2 per tree. | Min 400 mm deep at 500 mm max spacing | 150 mm in disturbed grassed areas | Min 300 mm deep, max 500 mm spacing | - |
| Notes: • Disturbed areas include any area of cut batter, fill batter, site of excavation (including borrow pit), site of dumping (including fill mound), drains, swales or area driven over by machinery resulting in soil compaction. Disturbed areas also include any areas where topsoil is effectively absent or areas of soil with dry bulk density exceeding the maximum shown in Table 720.072. • Undisturbed areas are those areas with the pre construction soil profile retained intact, without compaction or soil loss. • Initial ripping in granitic soils should be parallel to the contour. • Topsoil on grassed verge areas shall be left firm. |

(a)	Soil Additives including Gypsum

Soil additives, including any material used to modify the chemical properties of the soil, shall be applied by the Contractor prior to physical ripping and cultivation and in accordance with results and recommendations from site topsoil analysis tests.

The Contractor shall supply and install gypsum to the subsoil where subsoils are dispersive (AS 4419 5.11) to ensure soils are not dispersive, incorporating gypsum during ripping to a minimum depth of 300 mm.

The Contractor shall adjust the soil pH if the soil, including subsoil, to a depth of 300 mm is not in the range of 5-8.

(b)	Ripping

Ripping shall occur when soil is at or approaching the plastic limit of dryness and shall be postponed when the soil is at or wetter than field capacity.  Narrow tines shall be used in rocky ground and winged tines in other ground types.

Rock and rubbish brought to the surface shall be removed and disposed off.  The Contractor shall inform the Superintendent of sites where the presence of rock prevents the specified minimum ripping depth being achieved and implement alternative techniques (such as a standard tine) to maximise planting bed ground preparation depth.

In the vicinity of woody plants with trunk diameter greater than 600 mm at breast height that are to be retained, a protected area shall be marked at 1.5 times the height of the tree measured horizontally from the tree trunk. For trees less than 600 mm diameter the protected area shall be the area within the dripline. No ripping shall occur within the protected areas with any planting to be done using hand cultivation techniques to minimise damage to existing tree roots zones.

Where existing planting beds are to be extended, the unplanted areas shall be ripped as described above.

(c)	Topsoil Application

Following subsoil preparation, topsoil shall be spread on planting areas and grassed areas.  Topsoil shall not be compacted.

Weedy site topsoil shall not be spread to other locations on the site.  Weedy topsoil shall be handled in accordance with the Contractor’s weed management procedures.

(d)	Cultivation

Cultivation shall be undertaken to break soil down to a tilth with 80% of the volume composed of clods less than 50 mm in diameter.  Cultivation equipment that might create a hard pan beneath the depth of cultivation (such as rotary hoes and other powered cultivators) shall not be used.  In the event of saturated ground conditions, cultivation shall be delayed until the ground has dried out to a suitable condition.  Where ripping and topsoiling is sufficient to allow easy manual excavation of soil to a depth of 300 mm or more, cultivation may be omitted.

Cultivation shall not occur within the protected areas marked existing woody plants.  Hand cultivation shall be used within root zones of trees to be retained.

(e)	Topsoil Finished Surface Levels

After cultivation and trimming, the Contractor may lightly compress topsoil for stability on slopes.  Vibrating plates shall not be used.  The Contractor shall ensure dry bulk density does not exceed that described in Table 720.052:

Table 720.052  Maximum Dry Bulk Density of Soils for Planting and Grassing

| Soil Texture (as determined by AS 4419) | Maximum Dry Bulk Density for Topsoils |
| --- | --- |
| Clay soils | 1.3 g/cm3 (1.4 g/cm3 on slopes steeper than 3:1) |
| Loams | 1.5 g/cm3 |
| Sandy soils | 1.7 g/cm3 |

The finished level of grassed areas shall be:

(i)	not higher than 125 mm below weep-holes or damp-proof courses in adjacent walls;

(ii)	level with the bottom of fence plinths;

(iii)	level with adjacent pavements, kerbs, pits and other structures.

The finished level of garden bed mulch and/or topsoil shall be tapered so that the finished mulch and/or topsoil levels meet flush with the adjacent surfaces.

The Contractor shall ensure these conditions are maintained and there is no compaction of prepared soils before planting.

HP	The Contractor shall make available each ripped, topsoiled and cultivated planting area, individual tree planting and grassing area for inspection by the Superintendent and Independent Expert prior to mulching, planting or grassing.

(f)	Existing Planting Areas

Existing planting areas shall exclude areas of naturally occurring remnant vegetation.

Prior to undertaking site preparation or planting within existing plantations, all dead, severely damaged (<40% intact canopy) and fallen trees and shrubs shall be removed from the plantation.  Woody weeds with any seed or vegetative material capable of regeneration are to be removed and disposed of-off-site.

Any severely pest affected vegetation that cannot be successfully treated using pesticides (or any other treatment) shall be removed and disposed of off-site.  All remaining vegetation within the plantation is to be retained and protected from direct and indirect damage from ground preparation, weeding, mulching and infill planting.

Remaining vegetation in the existing plantation shall be assessed for damaged, dead or diseased limbs and branches.  All such limbs and branches on existing vegetation with a diameter greater than 50 mm in urban areas and 100 mm in rural areas are to be removed.  All pruning works including dead-wooding, canopy uplifting and weight reduction shall comply with the requirements of AS 4373.

720.06	MULCHING

(a)	Wood Mulch (Shredded or Chipped)

The Contractor shall install wood mulch to all Planting Areas unless otherwise specified.  Mulch shall extend at least 1 metre beyond plant centres at the outer edges of all Planting Areas and where this cannot be achieved in median, separator or splitter-island plantings, mulching shall extend to the back of kerb.

The Contractor shall install 2 metre diameter mulch rings around all Individual Tree Plantings.

Mulch depths in all situations shall be a minimum 125 mm and maximum 175 mm.

Mulch shall be raked to an even, neat appearance and kept clear of plant stems to avoid collar rot.

(b)	Weed Control Mat and Erosion Control Mat

The Contractor shall install weed control mat for planting areas steeper than 2:1 and in planting areas prone to flooding or within 2 m of waterways, swales, wetlands and sedimentation ponds or elsewhere as specified.

720.07	PLANTING

(a)	Planting

The Contractor shall carry out planting so as to ensure healthy, vigorous growth of plants. In the event the specified plant is unlikely to be suited to the as-constructed growing conditions, the Superintendent shall be notified.

Holes in heavy soils or on batters shall be prepared so as to ensure adequate drainage.

Holes shall not be left smooth sided in basalt or ‘plastic’ soils.  Drill or auger hole diggers shall only be permitted where soils have been cultivated.

Planting holes shall be backfilled with friable topsoil free of debris, rocks and clods greater than 50 mm in diameter.

(b)	Fertilising

The Contractor shall fertilise advanced trees and as determined by soil testing other planting areas.

(c)	Initial Watering

The Contractor shall saturate each plant within 8 hours after planting.  Cells and tubes shall be irrigated with a minimum 3 litres of water per plant.  Other container sizes shall be irrigated with a volume of water greater than the container size.

Under no circumstances shall any plant be planted into a dry planting hole (soil moisture at wilting point or drier).  If the soil is dry, the planting hole shall be saturated with water prior to planting.

720.08	GRASSING

(a)	Seeded Grassing

The Contractor shall seed grass to:

•	all areas indicated to be grassed on the Drawings, and

•	all areas disturbed by the Contractor which will not be a planting area or managed as remnant indigenous vegetation.

Grass seed shall be sown at minimum 100 kg/Ha (if drilled) or 200 kg/Ha (if broadcast), distributed evenly to achieve an even and dense grass cover.

Germination rate shall be minimum 80% cover within 8 weeks and 95% cover within 3 months of sowing.  If germination has not been achieved in any grassed area within 8 weeks, then the area(s) shall be reseeded with the specified grass seed mix.

(b)	Fertilising

Where deemed necessary by the independent expert the Contractor shall apply fertiliser evenly over the prepared surface.

(c)	First Mow

The Contractor shall carry out the first cut when at least 50% of the grassing area to be cut has grown to minimum 75 mm and maximum 150 mm height.  Mow to a minimum height of 75 mm.  Less than 1/3 the height of the grass shall be removed in the first cut.

720.09	LANDSCAPE MAINTENANCE

(a)	Scope of Maintenance

The Contractor shall provide a Landscape Maintenance Plan detailing the activities required to maintain the Plant Performance Requirements, with provision for future maintenance activities.

The Contractor shall implement the Landscape Management Plan and the requirements of this specification throughout the contract period.

***	Maintenance of the landscape work shall include the following tasks:

(i)		replanting

(ii)		weed control

(iii)		watering

(iv)		mowing/slashing

(v)		reseeding of seeded grass areas

(vi)		pest and disease control

(vii)		re-mulching

(viii)		pruning

(ix)		maintaining the site in a neat and tidy condition

(x)		repair and removal of tree guards and stakes

(xi)		repairs to erosion affected areas

(xii)		stockpile areas.

(b)	Maintenance Program and Joint Inspections

***	The Contractor shall prepare and submit a maintenance program showing sufficient information to enable the landscape maintenance works to be evaluated and shall show as a minimum the following:

•	inspection visits during the period of maintenance;

•	maintenance works during the period of maintenance including an outline of replacement planting regime and proposed pest and weed management activities.

Quarterly joint inspections shall be undertaken each year by the Contractor and the Superintendent after commencement of the Defects Liability Period.

Any remedial work shall be performed within three weeks of the date of inspection.  Grassing and planting may be delayed until suitable conditions prevail subject to independent expert advice and the approval of the Superintendent.

(c)	Plant Performance Requirements

Shrub and groundcover planting bed areas shall achieve the following performance requirements:

***	Table 720.091   Performance Requirements for Shrub and Groundcover Planting Areas

| 12 months after Practical Completion | 24 months after Practical Completion |
| --- | --- |
| • minimum ##:25% ground closure | • minimum ##:60% ground closure |
| • all plants showing healthy growth | • all plants showing healthy growth |
| • performance indicating probable ##:90% ground closure at 36 months after Practical Completion | • performance indicating probable ##:90% ground closure at 36 months after Practical Completion |

Planting that does not meet the above performance requirements shall be re-mulched and replanted annually to 100% of the original planting density for the area of planting area gaps.

Tree planting areas shall achieve the following performance requirements:

Table 720.092  Performance Requirements for Tree Planting

| Previous 12 months rainfall | Minimum Growth Rate Tubes/Cells | Minimum Growth Rate Advanced Trees |
| --- | --- | --- |
| More than 700 mm | 750 mm per annum | 300 mm per annum |
| 500 – 700 mm | 500 mm per annum | 200 mm per annum |
| Less than 500 mm | 400 mm per annum | 100 mm per annum |

Tree planting that does not meet the above performance requirements shall be replaced annually to achieve 100% of the original specified planting numbers.

Where planting does not meet the performance requirements because of soil conditions, the site shall be re-prepared and replanted at the Contractor’s expense.

(d)	Maintenance Tasks

The Contractor shall maintain the works as follows in accordance with the requirements of this specification, the drawings and plant schedules.

(i)	Declared Weeds and Weeds to be Removed

Eradication of declared weeds and weeds to be removed over the whole site shall commence from the date of Possession of Site.  The weed eradication targets shall be achieved within six months of Possession of Site and then shall be maintained.

***			The Contractor shall eradicate:

•	all state prohibited weeds

•	all regionally prohibited weeds

•	all regionally controlled weeds

•	the following Weeds of National Significance (WONS):

-	## (specify):

•	the following priority weeds identified in the local Catchment Management Authority Weed Action Plan:

-	## (specify):

(ii)	Mown Grass Weed Control

Weeds within grass areas are to be managed from cultivation of new grass areas.

Mown grass shall be maintained to control broad leaf herbaceous and woody weed populations.  Weed control shall be implemented to control broad-leaf weeds that exceed 10% cover in urban areas or 20% over in rural areas. Weed control shall occur prior to the weed plant reaching flowering.

Areas of native broadleaf cover among mown grass shall be brought to the attention of the Superintendent prior to spraying.  The Superintendent will direct whether these areas shall be treated.

Bare ground that results from weed control activities shall be cultivated and re-grassed to establish a minimum 95% grass cover.

(iii)	Weed Control in Planting Areas and Individual Tree Plantings

Weeds within planting areas and around tree plantings are to be managed from when cultivation of the planting site is complete.

All planting areas shall be managed by the Contractor to maintain a minimum of 90% weed free surface with no weeds taller or broader than 200 mm at all times and all weeds are to be removed prior to the production of viable seed.  Weeds within Individual Tree Plantings are to be managed for a radius of not less than 1.5 metres at each planting location.

(iv)	Pest Animals and Diseases

The control of pests and diseases shall begin before the first planting.  The Contractor shall maintain all plants free of insect infestation and plant disease so that healthy, vigorous plant growth is sustained.  Minor infestations of native pests and diseases on indigenous plants not threatening survival or healthy growth need not be controlled.

The Contractor shall provide protection to plants from vertebrate grazing animals.  All planting killed by grazing animals shall be replaced.  If more than 5% of planting in a planting area shows signs of damage by grazing animals, the Contractor shall take immediate action to prevent further grazing damage.  As a minimum the Contractor shall immediately install tree guards or suitable protective fencing securely around all plants subject to vertebrate grazing.

Where chemical repellents are to be used to prevent grazing, the repellent shall be applied until the growing tip of the plant is beyond the grazing height of the pest animal.

(v)	Replanting

Maintenance for replanting shall begin as soon as planting has begun in a planting area.

Plants which die or do not achieve the specified growth performance shall be replaced and replanted.

The Contractor shall program and allow for the propagation and supply of plants for any replanting during the current or next available planting season.  A full pass of replanting shall occur at least once in each year of the Defects Liability Period. Replanting shall be undertaken either in Autumn during the months of April or May or Spring during the months of September or October.  Replanting outside of these times can be undertaken subject to independent expert.

(vi)	Watering

The Contractor shall water all plants as necessary to ensure continued healthy and vigorous growth from time of planting.

(vii)	Grass Mowing ##(specification writer to strikethrough one of the following and delete this comment):

***			Mowing of all grass areas shall commence from Possession of Site.

***			Mowing of all grass areas shall commence from the earlier of sowing or road opening to traffic.

In addition to areas grassed by the Contractor, the Contractor shall maintain all other grassed areas within the limits of work in accordance with Roadside Maintenance Specification R76.4.2 –Mowing General.

Areas with less than 95% grass cover (for each grassed area) within three months after sowing shall be re-sown by the Contractor.  The Contractor shall ensure that 95% cover is maintained throughout the duration of the maintenance period.

(viii)	Re-mulching

Maintenance of areas mulched shall begin from the first planting.

Areas mulched with shredded wood mulch that do not have full foliage cover at ground level shall be maintained at a minimum consolidated depth of 75 mm by the Contractor. Re-mulching is not required where shrub or groundcover canopies have fully connected foliage.

(ix)	Pruning

Pruning maintenance shall begin from the first planting.

The Contractor shall prune trees and shrubs to remove damaged limbs and branches with a diameter above 10 mm. Tree branches likely to form a dominant ‘U’ or ‘V’ shaped crotch shall be pruned to a single leader.  All pruning and removal of living or dead stems greater than 10 mm diameter shall be in accordance with AS 4373 Pruning of Amenity Trees.

(x)	Maintaining the Site in a Neat and Tidy Condition

At any time the site is accessible to the public, the Contractor shall keep the site in a neat and tidy condition free of litter, debris or extraneous materials not associated with the works.  Litter that may be carried from the site by wind or water shall be controlled, collected and removed by the Contractor from Possession of Site.

(xi)	Maintenance of Tree Guards and Stakes

Maintenance of tree guards and stakes shall begin from installation.

Tree guards shall be maintained by the Contractor to ensure healthy vigorous plant growth is not inhibited.  Tree guards shall be removed when the plant reaches 750-1000 mm in height.  Tree guards shall be removed prior to Final Completion of the Contract unless otherwise directed by the Superintendent.

Marker stakes shall be removed when the plant reaches the height of the stake.

(xii)	Repairs to Erosion Treated and Affected Areas

Maintenance and repairs to erosion treated and affected areas shall begin from the earlier of installation of treatment or erosion occurring.

The Contractor shall maintain all areas of erosion protection treatments from the earlier of installation of treatment or erosion occurring and shall repair all damage or erosion which arises.  Such areas shall be re-prepared and re-protected as necessary to minimize erosion occurring and to establish a stable condition.

(xiii)	Intervention Standards

***			In addition to the above requirements, the Contractor shall maintain the landscaping works in accordance with the Intervention and Rectification Standards specified in R76 Roadside Maintenance for:

•	Surface Drains and Verges

•	Grass Mowing

•	Edge Trimming

•	Grass and Weed Control

•	Tree and Shrub Management

•	Declared Weed Control

•	Litter Control.

Appendix A - GRASS SEED PROPERTIES

| TYPE A Species | TYPE A STABILISATION MIX FOR REDUNDANT ROADS, SURFACE DRAINS AND PREPARED EMBANKMENT BATTERS Ryecorn* Perennial ryegrass (diploid) 1 Italian ryegrass (diploid) 2 Chewing Fescue Hard Fescue** Sheep Fescue** White clover (small-medium leaf) 3 Yanninicum sub clover 4 Browntop Bent Red Creeping Fescue | Proportion by weight 15-30% 15-18% 15-18% 5-8% 5-8% 5-8% 5-7% 5-6% 5-6% 5-6% |
| --- | --- | --- |
| TYPE B – 1 Species | TYPE B -1 STABILISATION MIX FOR EARTHWORKS WITH SLOPES STEEPER THAN 1V:3H Turf type tall fescue 5 Chewing fescue Hard Fescue Ryecorn* | 78% 10% 10% 2% |
| TYPE B - 2 Species | TYPE B – 2 STABILISATION MIX FOR EARTHWORKS WITH SLOPES STEEPER THAN 1V:3H – SHADE TOLERANT MIX Creeping red fescue Hard or sheep’s fescue Chewing fescue Ryecorn* | Proportion by weight 38% 30% 30% 2% |
| TYPE C Species | TYPE C TRAFFIC ISLAND AND MEDIANS Perennial ryegrass (diploid) 1 Chewing Fescue Turf ryegrass Hard Fescue** Sheep Fescue** White clover (small-medium leaf) 3 Yanninicum sub clover 4 Red Creeping Fescue | 17% 8% 26% 8% 8% 17% 17% 8% |
| Minimum Seed Purity 98% and shall not contain declared weed seed |
| Minimum Germination Rate 90% at date of supply |
| Notes | *Rate of ryecorn application is dependent on the expected erodibility of the surface, the appropriate rate should be determined during development of the landscaping plan and/or the erosion and sediment control plan. The rate may be increased to a maximum of 30% for highly erodible soil types. Mowing is to be performed strictly in accordance with 720.10(c), to ensure that the permanent crop is not suppressed by the ryecorn cover-crop. **depending on availability either variety may be used alone at a rate of 10-16% 1. Perennial ryegrass (diploid) varieties include Rohan, Nui, Kidman, Victorian. 2. Italian ryegrass (diploid) varieties include Concord, Hulk, Crusader, Tempo. 3. Yanninicum sub clover varieties include Monti, Gosse, Trikkala 4. White clover (small-medium leaf) varieties include Apex, Pitau, Tahora, Weka, Huia. 5. Turf type tall fescue varieties include RTF, Barrobusto |

# Text boxes

Department of State Growth – May 2022

Section 720 (Page 1 of 14)

Department of State Growth – May 2022

Section 720 (Page 2 of 14)

Department of State Growth – May 2022

Section 720 (Page 3 of 14)

Department of State Growth – May 2022

Section 720 (Page 4 of 14)

Department of State Growth – May 2022

Section 720 (Page 5 of 14)

Department of State Growth – May 2022

Section 720 (Page 6 of 14)

Department of State Growth – May 2022

Section 720 (Page 7 of 14)

Department of State Growth – May 2022

Section 720 (Page 8 of 14)

Department of State Growth – May 2022

Section 720 (Page 9 of 14)

Department of State Growth – May 2022

Section 720 (Page 10 of 14)

Department of State Growth – May 2022

Section 720 (Page 11 of 14)

Department of State Growth – May 2022

Section 720 (Page 12 of 14)

Department of State Growth – May 2022

Section 720 (Page 12 of 14)

Department of State Growth – May 2022

Section 720 (Page 13 of 14)

Department of State Growth – May 2022

Section 720 (Page 14 of 14)

Department of State Growth – May 2022

Section 720 Appendix A